## Slide 1: GSM Networks

## Slide 2: GSM
Global System for Mobile Communications
NMT = Nordic Mobile Telephone
AMPS = Advanced Mobile Phone System
GSM = Global System for Mobile communication
CSD = Circuit Switched Data
HSCSD = High Speed Circuit Switched Data
GPRS = General Packet Radio Service
EDGE = Enhanced Data Rates for GSM Evolution
UMTS = Universal Mobile Telecommunication System
LTE = Long Term Evolution
 | 1G | 2G | 2.5G | 3G | 4G
Timeline | ‘80 | ‘90 | ‘00 | ‘02 | ‘08
System | NMT, AMPS | GSM/CSD | HSCSD, GPRS, EDGE | UMTS | LTE
Transfer | - | kb/s | x | 384 kb/s | 300Mb/s

## Slide 3: GSM architecture

## Slide 4: Acronyms
MS – Mobile Station
BSS – Base Station Subsystem
  BTS – Base Transceiver Station
  BSC – Base Station Controler
NMS – Network Management System
NSS – Network & Switching Subsystem
  MSC– Mobile Switching Center
  GMSC – Gateway Mobile Switching Center
  HLR – Home Location Register
  VLR – Visitor Location Register
  AuC – Authentication Center
  EIR – Equipment Identity Register

## Slide 5: Network Areas
Cell
  One BTS covers one cell
  Identified by Cell Global Identity
Location Area
  A group of cells served by BTSs controlled by one BSC
MSC/VLR Service Area
  Area covered by one MSC
PLMN
  Whole area covered by one network operator is the Public Land Mobile Network

## Slide 6: Mobile Station
Physical device:
  Radio transceiver
  Display + keyboard, battery ..
  SIM card
    Subscriber Identity Module
      Subscriber identification
      addressing information
Functions
  Voice services
  Data bearer services
  Supplementary services

## Slide 7: Base Station Subsystem (BSS)
Base Transceiver Station (BTS)
  Connects the Mobile Station to the cellular network
  Handles radio interface protocols
  Modulates, demodulates and ciphers
  Physically: Antennas + transceiver
  Serves a Cell
Base Station Controller (BSC)
  Controls a group of BTS
  Manages radio resources – e.g. allocates communication channels, handovers, power control, signal quality

## Slide 8: Networking Switching Subsystem (NSS)
The Core Network
MSC + VLR + HLR + other nodes connected to those via signaling protocols

## Slide 9: HLR
Home Location Register
Database and Service
  Subscriptions
    Administrative information
      IMSI + MSISDN
      Supplementary services
      Basic service subscription information
      Service restrictions – e.g. roaming permission, call barring..
    Location information
Registers users in the network
Holds location information of mobile stations under the form of the VLR address of the VLR that currently serves a the subscriber

## Slide 10: VLR
Visitor Location Register
To a certain extent it is a cache of HLR
Contains a subset of administrative information necessary for call control of mobile stations within the are controlled by the VLR
  Data stored only while subscriber is in the area
    Subscriber profile
    Authentication data
    Special numbers IMSI, TMSI, MSRN
Each MSC has a VLR, usually in the same box
Does
  Location update when subscriber enters the area
  Removes data when subscriber exits the area
  Manages local subscriber data

## Slide 11: EIR
Equipment Identity Register
  Allows/disallows a certain mobile equipment in the network
  Mobile equipment is identified by IMEI – International Mobile Equipment Identity
  Lists of IMEI numbers
    White list – accepted device list
    Black list - blocked devices due to stolen, fraud, etc.
    Grey list - incompatible devices, bugs, etc.

## Slide 12: AuC
Secure database holding secret keys
Secret key is stored both places:
  In the SIM module
  In AuC database
Does:
  Authentication
  ciphering

## Slide 13: MSC
Mobile Switching Centre
More BSC are connected to one MSC
Responsible with:
  Routing of incoming/outgoing calls
  Billing (CDR – call detail record)/authorization of calls
  Handling mobile station management:
    Registration
    Authentication
    Location update
    Handovers
    Call routing

## Slide 14: GMSC
GMSC
  Gateway MSC
  Link to other networks mobile or not
  Terminates calls

## Slide 15: Addressing
GSM
  User != Equipment
  User subscribes to multiple services
  Designed for security up to a certain extent
  Subscriber Id != phone number

## Slide 16: Addressing - IMEI
International Mobile Station Equipment Identity
Identifies the equipment
Allocated by manufacturer
Registered by the network and stored in EIR in order to recognize equipment as:
  Compatible/incompatible
  Old or obsolete
  Stolen!
IMEI = TAC + FAC + SNR + SP
  TAC – Type Approval Code 6 decimal, e.g. 10,20 – Nokia; 51 - Sony
  FAC – Final Assembly Code 6 decimal
  SNR - Serial Number 6 decimal
  SP – Spare 1 decimal
Theoretically should be unique
  Practically: India 2012 - 18000 devices with the same IMEI were found
Exercise : dial *#06# on your phone to get your IMEI

## Slide 17: Addressing - IMSI
International Mobile Subscriber Identity
Identifies the Subscriber
Stored in SIM card and HLR
IMSI = MCC + MNC + MSIN
  MCC – Mobile Country Code 3 decimal
  MNC – Mobile Network code 2 decimal
  MSIN – Mobile Subscriber Identification Number 10 decimal(identifies the subscriber)

## Slide 18: Addressing - MSISDN
Mobile Subscriber ISDN Number (ISDN = Integrated Services Digital Network)
This is the telephone number
One phone - many SIM cards
  One subscriber identified by one IMSI can hold more MSISDN for different services
  IMSI,MSISDN pair is stored in HLR
MSISDN = CC + NDC + SN
  CC – Country Code max 3 digits
  NDC – National Destination Code max 3 digits
  SN – Subscriber Number max 10 digits

## Slide 19: Addressing - MSRN
Mobile Station Roaming Number
Temporary ISDN number assigned by the VLR to the mobile station based on location
Same structure as MSISDN
Allocation of MSRN by VLR:
  On registration when entering a new Location Area;
  As per HLR request
  Dynamically at call setup
MSRN is further stored in HLR
Used for routing calls to the mobile station
Hides the real MSISDN for traffic sniffers

## Slide 20: LAI
Location Area Identity
Each Location Area in the PLMN has an ID
LAI = CC + MNC + LAC
  CC – Country Code 3 digits
  MNC – Mobile Network Code 2 digits
  LAC – Local Area Code 5 digits
Notes: http://cellphonetrackers.org/gsm/gsm-tracker.php
http://www.cell2gps.com/

## Slide 21: Addressing – TMSI
Temporary Mobile Subscriber Identity
Assigned by the VLR
Stored only in VLR
Stored in Mobile Station
Only local significance at VLR service area and only for how long subscriber is handled by this VLR
Used to hide the identity of the subscriber if radio channel is listened to
Along with Location Area Information uniquely identifies the subscriber (TMSI, LAI)
LMSI – Local Mobile Subscriber Identity – can be assigned by VLR as an additional search key to speed up database searches

## Slide 22: Authentication of Mobile Station

## Slide 23: Authentication
Mobile Station requires to attach to the network
Mobile Station and AUC share the same secret key Ki
MSC sends the AUC the IMSI of the subscriber
The AUC computes and sends back to MSC:
  A random number to be used as challenge (rnd)
  The response to the challenge (sres)
  A session key (Ks)
MSC challenges the MS with the random
MS computes the response to the challenge (res) and sends it to MSC
MSC checks if res==sres
If so, the MS is allowed in the network
MS can easily derive session key itself (Ks); MS switches to ciphering mode
Ks is used to encrypt communication radio between MS and network using A5 algorithm

## Slide 24: Location Update - attach

## Slide 25: Location Update - attach
MS wants to register at current location and sends a request with its IMSI and LAI (MCC+MNC+LAC)
Authentication takes place as presented
MSC/VLR assign a MSRN to the MS and update HLR with new identification information
HLR sends VLR subscriber data for local caching
HLR confirms to MSC, and MSC confirms to MS
VLR generates TMSI for subscriber
After ciphering the connection, the TMSI is updated into the MS; this way TMSI is not compromised

## Slide 26: Location Update – when moving

## Slide 27: Location Update
When subscriber enters an area covered by other MSC/VLR
VLR finds no record of MS; asks to HLR to give details and update location
HLR sends subscriber data to VLR for local storage and
HLR instructs the old VLR to forget the MS
The rest of the flow is the same as for the area

## Slide 28: Handovers
1,2 involves BSC
3 involves MSC
4 involves MSC, HLR (Location Update)

## Slide 29: Voice Calls
Mobile to Mobile same network different MSC

## Slide 30: Voice Call
A Party diales number MSISDN B
SRI Request – MSC of A Party asks HLR how to address dialed number; HLR knows location information therefore knows MSC/VLR of B, i.e MSC/VLR B
Provide Roaming Number Request – HLR asks VLR B about MSRN of B
SRI Response – MSC A is informed how to reach MS B, i.e. what MSC, what MSRN
A connection is established between the MSC A and MSC B
Initial Address Message – MSC A dials the MSRN B directly to MSC B, informing that A Party wants to call B
Alert – notify that MS B is ringing, A is also played the ring tone
Answer– MS B answers the phone; voice channels are connected
Release – one of the parties hangs up

## Slide 31: Roaming
HPLMN
HLR
MSC
GMSC
VPLMN – Visited Country
HLR
MSC
GMSC
VPLMN – Home Country
HLR
MSC
GMSC
PLMN – Public Land Mobile Network
HPLMN – Home PLMN (Home network of SIM card)
VPLMN – Visited PLMN (Visited foreign network)

## Slide 32: Roaming
PLMN – Public Land Mobile Network
HPLMN – Home PLMN (Home network of SIM card)
VPLMN – Visited PLMN (Visited foreign network)
User attaches to:
  HPLMN
  VPLMN – home – i.e. local roaming
  VPLMN – foreign country – i.e. roaming abroad
In roaming participate:
  HLR in HPLMN
  VMSC in VPLMN
To make roaming happen:
  Operators must sign agreement
  Networks must be properly configured
  Roaming service must be activated for given subscriber (HLR profile)

## Slide 33: UMTS Network (3G)
UMTS = Universal Mobile Telecommunications System
  new technologically more advanced and more effective access to network – Wideband CDMA
  troughput for user up to 2Mbit/s
  Completely different access technology
  Different BTS (Node-B)
  Different BTS controllers (RNC)
  Different user terminals (supporting two systems)
  Voice codecs with adaptive coding (AMR)

## Slide 34: UMTS Network Diagram

## Slide 35: UTRAN
Node B
  Analogue to BTS
  Radio signal processing
    Modulation/demodulation
  Managing radio resources
  Power control
  Signal measurement / error rate
RNC (Radio Network Controller)
  Analogue to BSC
  Soft handover
  Ciphering
  Location of terminals
Interfaces
  IuPS – packet network connections
  IuCS – voice network connections

## Slide 36: GSM Interfaces

## Slide 37: GSM Interfaces Review
Um – MS to BTS radio interface
Abis – BTS to BSC – radio equipment control and
A – BSS to MSC channel management
B – MSCtoVLR – MSC interrogates VLR about MS in the area; protocol is MAP/B (SS7)
C – HLR to GMSC – exchange routing information; protocol is MAP/C
D – VLR to HLR; protocol is MAP/D for location exchange
E – MSC to MSC; handover and relay; protocol is MAP/E
F – MSC to EIR; check IMEI status
G – VLR to VLR; location update; protocol is MAP/G
H – MSC to SMS Gateway
HLR to USSD Gateway is also MAP based

## Slide 38: Security review
Subscriber authentication (algorithm A3, A8)
Network authentication (only UMTS, optional)
Signaling and voice ciphering (algorithm A5)
Controlling of used terminals (HLR, EIR)
Controlling of access to terminal – PIN code (ang. Personal
Identification Number)
Access to operator network for legal authorities (LI – ang. Lawfull
Interception)
Physical access to network elements
Using IPSec to secure IP links (sigtran)

## Slide 39: GPRS
General Packet Radio Service
Packet oriented data service – Packet transmission in radio link
Costs are dependent on data volume not duration
Mobile network is transparent to various IP networks
Services
  SMS
  MMS
  Internet access, Facebook, VPN

## Slide 40: GPRS Architecture

## Slide 41: SGSN
Serving GPRS support node
Tasks:
  Security – encryption
    Data is encrypted between mobile station and SGSN
  Routing packets
  Mobility handling, e.g. handover
  Records charging information

## Slide 42: GGSN
Gateway GPRS support node
Gateway
Router
Firewall
Authenticates user
Charging info
IP address assignment

## Slide 43: GPRS Call
Subscriber wants to access Internet
Subscriber has set up on phone upon subscription:
  APN (Access Point Name)
    Ex. Postpaid.operator.ro, prepaid.operator.ro
APN determines:
  IP network to which user can connect
  Set of parameters used in this connection
Gateway IP

## Slide 44: PDP Context
PDP = Packet Data Protocol
PDP context
  information about active user session
  MS IP Address
  GGSN used to access Internet
Steps
  Attach to network
  Activate PDP context

## Slide 45: PDP Context Activation

## Slide 46: PDP Context Activation
MS initiates procedure to obtain IP address, sends APN as parameter
SGSN queries DNS to find the IP of the GGSN corresponding to APN data
DNS replies with the GGSN IP
SGSN routes PDP creation request to the GGSN
GGSN queries Radius server to authenticate the user
GGSN responds SGSN indicating the procedure finished and an IP has been allocated
SGSN responds the MS with the IP
The MS can now browse

## Slide 47: LTE
GERAN – GSM Edge Radio Network (2G)
UTRAN – UMTS Network (3G)

## Slide 48: LTE
Long Term Evolution
Optimized for IP services
NO optimization for Voice (fallback to 3G)
MME
  Mobility Management Entity
    Serves control plane – session and subscriber management
P-GW
    PDN (Packet Data Network)
    Interface with external IP
    Analog to GGSN
S-GW
    Serving gateway – interface towards E-UTRAN (radio infrastructure for LTE)
    Analog to SGSN
PCRF
  Policy and Charging Rules Function
  Enforces policies, e.g. throttling download speed
HSS
  Equivalent to HLR

## Slide 49: Conclusion
In the Core Network most protocols are
  SS7 based:
    Various MAP
    CAP
  Diameter